trxpl_server:
=============
  (D. McCune Jan. 2010)
  (update D. McCune Nov. 2010)

Contents of this document:

  -- Introduction
  -- See also...
  -- Access to the software
  -- Prerequisites for use
  -- TRANSP input data
  -- Server initiation
  -- Plasma State request to server
  -- Server shutdown
  -- Additional notes
  -- Sample session output
  -- appendix: "trxpl2ps"


Introduction:
-------------

This software provides a convenient and reasonably efficient way for a client
code to request a sequence of Plasma State files (or "states") to be extracted 
from the output data of a completed TRANSP run, based on a simple process to 
process communications protocol on a single system.

The Plasma States are generated by "trxpl", an NTCC interactive fortran 
program configured to run as a service, connected to a pipe driven by a 
shell script that is polling for data request input files.

In this mode, "trxpl" remains memory resident and contains the entire time
variation of all the TRANSP data needed to construct any client specified 
time series of states.  "Light weight" state files (containing 1d profiles 
such as heating and current drive sources, plasma temperatures, densities, 
rotation velocity and pressure, but not full equilibrium data) can be 
produced on demand, with a delay of approximately 2 seconds per request.
This amount of time is due to polling and file I/O costs.  "Heavy weight"
states which include additional MHD equilibrium information take only 
slightly longer.

It should be noted that should 2 seconds prove an unacceptable delay, a higher
speed memory-based coupling could be done using library subroutine calls,
but, it would require linking a collection of TRANSP I/O libraries as well 
as MDS+ (plasma experimental data access systems library) into the driver 
code which wants to access the Plasma State time series from TRANSP data.


See also...
-----------

There is a library callable interface to the trxpl Plasma State 
extraction functionality.  It is contained in $NTCCHOME/lib/libtrxplib.a
and is demonstrated in the NTCC program, trxpl2ps.  The callable 
interface allows TRANSP data from selected run time slices to be 
loaded directly in memory inside a Plasma State object provided by 
the driver program.

For more information see the appendix "trxpl2ps".


Access to the software:
-----------------------

"trxpl" and associated driver scripts are distributed through the NTCC.  This
software is contained in the "trxplib" and also in the "tr_client" modules
in the NTCC catalog.  The NTCC "xplasma" and SciDAC "plasma state" modules
will be included in the download, along with all needed TRANSP I/O libraries.


Prerequisites for use:
----------------------

(1) The NTCC software must be built.  For this, NetCDF and other systems 
libraries as well as a suitable fortran compiler are required.  For remote 
access to TRANSP data, the system must provide access to the MDS+ shareable 
C library which is common to all US tokamak experimental sites and is 
maintained and supported at the MIT Plasma Fusion Science Center.

(2) Users must have permission for remote (MDS+) access to the TRANSP data.
Each institution's TRANSP MDS+ archive has its own rules for data access 
permission.  Unless prior arrangements have been made, a new user will 
need to request access permission.

PPPL experts support NTCC software builds at various labs and computer
centers:  PPPL, ORNL, NERSC, General Atomics, MIT, IPP/Garching, JET/Culham.
We have a limited ability to respond to requests for additional support.

Contacts:  Doug McCune                 dmccune@pppl.gov
           Christiane Ludescher-Furth  ludesche@pppl.gov

These contacts can also be used to request permission for access to TRANSP
MDS+ data on the PPPL server TRANSPGRID.PPPL.GOV.  With the exception of 
PPPL archived JET data, permission for access is routinely granted.  (Access 
to JET data requires a negotiation with EFDA authorities, agreement to prior
review of publications, etc.).


TRANSP input data:
------------------

A path string is provided to identify TRANSP data stored in MDS+.  The
exact form of this string varies slightly, depending on the MDS+ server 
being contacted.

The general syntax is:  <MDS+-server>:<MDS+-treename>(<MDS+-runid>).

A typical path string for a run at the PPPL server would be:

   TRANSPGRID.PPPL.GOV:TRANSP_TFTR(TFTR.88,37065P35)

(For several tokamaks the 2 digit shot year code, ".88" in this example,
can be omitted).

A path string for a DIII-D TRANSP run on the General Atomics server looks 
like:

   ATLAS.GAT.COM:TRANSP(1112030485).

If MDS+ is unavailable (e.g. at a supercomputer center), then, the necessary 
set of TRANSP data files must be uploaded.  The most efficient means of doing 
this will vary depending on the archive, and, the set of files needed could 
evolve over time; additions to TRANSP output will eventually require breaking 
up the current TRANSP <runid>.CDF output file.  Even so, the necessary files
for modern runs are readily available from the PPPL archive file system:

   /p/transparch/result/<tok>/<yy>/<runid>PH.CDF -- TRANSP input data
   /p/transparch/result/<tok>/<yy>/<runid>.CDF -- TRANSP output data
   /p/transparch/result/<tok>/<yy>/<runid>TR.DAT -- TRANSP namelist data

For example: /p/transparch/result/TFTR/88/37065P35PH.CDF, etc., on the PPPL
Linux cluster (portal.pppl.gov).

If file access mode is used, the files must be uploaded to a known directory
readable by the "trxpl" server when this is launched.

NOTE: each TRANSP run represents a time dependent simulation of a certain time 
range of a tokamak plasma shot.  Of course simulation quality varies, and,
for "famous" shots dozens or even hundreds of TRANSP simulations may be
archived.  The TRANSP run author should be consulted for guidance, i.e. to 
identify the specific simulation best suited to a particular purpose.


Server initiation:
------------------

Use "trxpl_server", an executable shell script provided with the NTCC 
module containing trxpl.

For MDS+ access the server initiation command looks like this:

  trxpl_server INIT MDS+ <MDS+-path-to-TRANSP-data> <output-path> [mdescr]

For example:
  trxpl_server INIT MDS+ "transpgrid.pppl.gov:TRANSP_TFTR(TFTR.88,37065P35)" \
               xyz  TFTR_93.mdescr

...in which case output is written into subdirectory xyz of the current
working directory.

NOTE: "shot-year" auto-detection is available for some tokamaks, including
as of 2010 these: {AUGD, D3D, EAST, JET, MAST, NSTX, TFTR}.  When this is
available, it is possible to omit the shot-year from the MDS+ path.  So,
for example, the simplified MDS+ path string works here:

  trxpl_server INIT MDS+ "transpgrid.pppl.gov:TRANSP_TFTR(TFTR,37065P35)" \
               xyz  TFTR_93.mdescr

(Note omission of shot-year code ".88").

For file access the server initiation command looks like this:

  trxpl_server INIT FILE <path-to-TRANSP-data> <output-path>  [mdescr]

For example:
  trxpl_server INIT FILE /p/transparch/result/TFTR/88/37065P35 \
               abc  TFTR_93.mdescr

...in which case output is written into subdirectory abc of the current
working directory.

Note, the optional final argument [mdescr] (added DMC Nov. 2010) names 
a machine description file.  If specified, this is used as a source of 
data for neutral beam full-half-third energy fraction dependence on 
beam voltage.  The file is expected to be located in the directory

   $TRANSP_LOCATION/mdescr

at sites where NTCC software is installed.  This was added, because 
for processing of plasma state time series it is better to have the
full energy fraction tables available.

A note on machine description files:
------------------------------------

TRANSP runs imbed their own machine description (i.e. neutral beam
geometry, etc.) via the TRANSP namelist.  For historical reasons, most
TRANSP runs contain neutral beam lists consisting not of all available
neutral beams, but, only the subset which were energized for a given
shot.

Therefore, it is not safe to use a "generic" tokamak machine description
file to represent the beam geometries from a TRANSP run-- in general this
will only be correct for shots in which all heating beams were active.
This is a minority of actual shots.

The trxpl_server creates a usable subset machine description file.
After successful server initialization (INIT) command, this file is
to be found here:

   <output-path>/init_test.mdescr

where <output-path> matches the value given in the successful
"trxpl_server INIT ... " command.

Applications needing this information should copy/rename this run-
specific modified machine description, as required.

It is recommended to use the [mdescr] optional argument in the
trxpl_server INIT command, and to give the generic tokamak machine
description file covering the selected shot.  This machine description
can then provide the full beam injection full-half-third energy fraction
data (a set of tables vs. beam voltage) which cannot be acquired from
the TRANSP run alone.  If this step is omitted, the beam fractions 
will be based on their values from a single point in time, i.e. the
time dependence of this data will not be handled correctly.


Plasma State request to server:
-------------------------------

To request a Plasma State file from an active server:

  trxpl_server FETCH <time> <output-path> <filename>

For example:

  trxpl_server FETCH 4.225 abc tr_ps4x225

This results in the creation of the Plasma State file 

  abc/tr_ps4x225.cdf

which contains the data at t=4.225 seconds, extracted from the TRANSP run
to which the server for directory abc is attached.


Server Shutdown:
----------------

To de-activate a trxpl server, do this:

  trxpl_server KILL <output-path>

For example,

  trxpl_server KILL abc

...to kill the server that has been writing Plasma State files to the abc
subdirectory.


Additional notes:
-----------------

If MDS+ access is used, a disk cache of MDS+ accessed data is created.  This
way, the remote MDS+ server only has to be accessed once, during the first
server initiation, even if a time dependent simulation is halted and restarted.
This results in faster I/O speeds and better reliability, after initial contact
with the MDS+ server.

By default, the server cache data is written under the hidden subdirectory

  $HOME/.rplot_cache

This can be overridden by setting the environment variable RPLOT_CACHE to
an existing, writable directory.  If this is done the .rplot_cache sub-
directory is written under the directory so named.

Multiple concurrent trxpl servers can co-exist, provided each is using a
distinct output directory.

It is up to user processes to KILL trxpl_server jobs when done; otherwise
"zombie" trxpl processes will persist and use up memory.

Here are the shell scripts used:

   trxpl_server  (launch/use/stop a trxpl server)
   uread_server  (launch/use/stop a "uread" interactive fortran program)
   uread_send_wait  (communicate with server and wait for replay)
   ichannel  (pipe input to memory resident server)

And "uread" scripts specific to trxpl:

   tr_playback_init.ind
   tr_playback_start.ind
   tr_playback.ind


Sample session output:
----------------------

--> Here is an example of results of a FILE based trxpl_server session.  In
this session, on the PPPL cluster, a specific PPPL archived TRANSP run 
is accessed, and extracted state files are stored in a subdirectory "abc":


>>> trxpl_server INIT FILE /p/transparch/result/TFTR/88/37065P35 abc

 INIT syntax OK: FILE /p/transparch/result/TFTR/88/37065P35 abc abc/trxpl_comm 
trxpl_server INIT -- I/O test; load MDS+ cache...
/usr/pppl/transp/local/dmccune/rhel4/exe/trxpl @tr_playback_init /stype=heavy /mode=FILE /path="/p/transparch/result/TFTR/88/37065P35" /time=0.0 /wpath="abc/init_test" /spath="abc/sawtimes.dat"
  
  TRXPL version update: 31 Dec 2009
  D. McCune, 2000--2009: TRANSP time slice extractor.
  
 @FILENAME=tr_playback_init.ind
  %urdopen: trying: TRANSP_LOCATION/tr_playback_init.ind
  %urdopen: trying: /u/dmccune/transp/codesys/tmi/trxpl/tr_playback_init.ind
  %initcpl:  MDS_CACHE enabled.
  dmg_datbuf_expand call from dmgini_sized: isize= 0
  ... reading NetCDF header data ...
  cdfhrd: size(time) =  2048
  cdfhrd: size(time3) =  2048
  %trx_connect_tlims: no sawteeth found.
  %trx_connect: probing for free boundary data.
  (no free boundary data).
  
  trxpl:  connected to run FILE:/p/transparch/result/TFTR/88/37065P35
   time range (seconds):   3.00100E+00  5.10000E+00
    #time pts: scalars:  211 ; profiles:  211
  
  (no free boundary data).
  
  path:  FILE:/p/transparch/result/TFTR/88/37065P35

  time of interest:   3.000999927520752
  +/- averaging time:  0.E+0
  # of theta pts:     151
  # of R pts:         101
  # of Z pts:         101
  Btoroidal orientation is set from TRANSP data     
  Plasma current orientation is set from TRANSP data     
  (R,Z) grid extent:  to match limiters.
  %t1mhdeq:  reading scalars...
  %t1mhdeq:  reading profiles...
  %eqm_bset: equilibrium specification completed.
  tokdev = "TFTR"
  run_label = "TFTR.88 37065P35                        "
  %trxpl: Rmin reset to safely enclose inner bdy of plasma.
   old Rmin:  1.6560000610351562  new Rmin:  1.5723652403936228
  ps_init_tag: Plasma State v2.023 f90 module initialization.
  trx_init_state status =  0
  GEQ FILE:   abc/init_test.geq
  STATE FILE: abc/init_test.cdf
  MACHINE DESCR: abc/init_test.mdescr
  SHOT CONFIG:   abc/init_test.sconfig
  
  %trx_gen_state: building state from TRANSP data.
  
  %trx_gen_state: no angular velocity found; assuming ZERO rotation.
  %ps_update_fromxplasma: allocating nr,nz  =  109 , 109
  %ps_update_fromxplasma: allocating nlim   =  202
  %ps_mhdeq_nclass: allocating 16 Pfirsch-Schlutter moments profiles.
  %plcexec:  command execution starting:  SAVE      
  %plcexec:  command execution starting:  SAVE      
  %plcexec:  command execution starting:  SAVE      
  %plcexec:  command execution starting:  SAVE      
  %plcexec:  command execution starting:  SAVE      
  %plcexec:  command execution starting:  SAVE      
  %trx_gen_state: edge data available, T0recyc =  1.00000E-02 KeV.
   T0gasfl =  3.00000E-03 KeV.
   OM0recyc =  0.00000E+00 rad/sec.
   OM0gasfl =  0.00000E+00 rad/sec.
  %trx_gen_state: TRANSP namelist available; splitn loaded.
  %trx_gen_state: TRANSP input data available; trdatbuf loaded.
  %trx_gen_state -- source averaged data used for
   recycling and gas flow source neutral densities.
  trx_gen_state completed, status =  0  (0 is normal).
2.158u 0.229s 0:03.25 72.9%     0+0k 40184+24io 54pf+0w
============
INIT TEST OK
============
uread_server init abc/trxpl_comm trxpl @tr_playback_start /mode=FILE /path="/p/transparch/result/TFTR/88/37065P35" /time=0.0
 %uread_server: trxpl communications directory: abc/trxpl_comm 
 %uread_server: trxpl launched... 
[1] 27126 27127
 %uread_server(debug) : wait_file = abc/trxpl_comm/prev_input.dat 
0.015u 0.048s 0:04.22 1.1%      0+0k 0+0io 0pf+0w
=======
INIT OK
=======


--> Here are the contents of the "abc" subdirectory after server initiation:

>>> ls abc
init_test.cdf  init_test.mdescr   sawtimes.dat
init_test.geq  init_test.sconfig  trxpl_comm


--> Here a named state file is requested at a particular time:

>>> trxpl_server FETCH 4.100 abc tr_ps4x100
FETCH syntax OK
uread_server send abc/trxpl_comm wait:abc/tr_ps4x100.mdescr @tr_playback /stype=light /time=4.100 /wpath="abc/tr_ps4x100" /key=normal
 %uread_server(debug) : wait_file = abc/tr_ps4x100.mdescr 
========
FETCH OK
========


--> Here are the contents of the "abc" subdirectory after this fetch:

>>> ls abc
init_test.cdf  init_test.mdescr   sawtimes.dat    trxpl_comm
init_test.geq  init_test.sconfig  tr_ps4x100.cdf


--> Here another fetch:

>>> trxpl_server FETCH 4.150 abc tr_ps4x150
FETCH syntax OK
uread_server send abc/trxpl_comm wait:abc/tr_ps4x150.mdescr @tr_playback /stype=light /time=4.150 /wpath="abc/tr_ps4x150" /key=normal
 %uread_server(debug) : wait_file = abc/tr_ps4x150.mdescr 
========
FETCH OK
========


--> Here are the contents of the "abc" subdirectory after this fetch:

>>> ls abc
init_test.cdf  init_test.mdescr   sawtimes.dat    tr_ps4x150.cdf
init_test.geq  init_test.sconfig  tr_ps4x100.cdf  trxpl_comm


--> And here the server is shut down:

>>> trxpl_server KILL abc
 KILL OK: abc abc/trxpl_comm 
 %uread_server: executing action: kill 


--> The server "communications subdirectory", which may contain useful
information for debugging, is found here:

>>> ls abc/trxpl_comm
ichannel.log      killed_pid.dat  prev_input.dat   trxpl.log
input_record.tmi  old_kill.dat    prev_input.dat~

--------------------

For an MDS+ invokation here is a similar command sequence:

>>> trxpl_server INIT MDS+ "transpgrid.pppl.gov:TRANSP_TFTR(TFTR.88,37065P35)" xyz
  ... ...

>>> ls xyz
init_test.cdf  init_test.mdescr   sawtimes.dat
init_test.geq  init_test.sconfig  trxpl_comm

>>> trxpl_server FETCH 4.200 xyz tr_ps4x200
  ... ...

>>> trxpl_server FETCH 4.225 xyz tr_ps4x225
  ... ...

>>> ls xyz
init_test.cdf  init_test.mdescr   sawtimes.dat    tr_ps4x225.cdf
init_test.geq  init_test.sconfig  tr_ps4x200.cdf  trxpl_comm

>>> trxpl_server KILL xyz

An attempt to fetch a state from a server that has been KILL'd will result in 
an error:

>>> trxpl_server FETCH 4.225 xyz tr_ps4x225
uread_server send xyz/trxpl_comm wait:xyz/tr_ps4x225.mdescr @tr_playback /stype=light /time=4.225 /wpath="xyz/tr_ps4x225" /key=normal
 ?uread_server: not found: xyz/trxpl_comm/progname.dat 
 ? trxpl_server -- FETCH failed. 


Appendix: "trxpl2ps"
--------------------

There is a library callable interface to the trxpl Plasma State 
extraction functionality.  It is contained in $NTCCHOME/lib/libtrxplib.a
and is demonstrated in the NTCC program, trxpl2ps.  The callable 
interface allows TRANSP data from selected run time slices to be 
loaded directly in memory inside a Plasma State object provided by 
a fortran driver program.

To use this subroutine library callable interface, the driver program
needs to be built with TRANSP data access subroutine libraries (all
available in the NTCC software distribution).  Once this is done,
however, there may be some reliability advantage, and definitely
there will be a performance advantage, to using the callable interface 
instead of the trxpl_server client-server hook up.

The trxpl2ps program has functionality similar to trxpl, but with no
graphics and just a command line interface.  Running the program with
no arguments causes a summary printout of the arguments expected.

The trxpl2ps program (with the -all_times command line option) can also 
used to simply pump out a complete set of Plasma State files covering 
the entire time range of the selected TRANSP run.  A trxpl2ps output
file "protimes.dat" gives the correlation between times and Plasma
State NetCDF file names.

Here is a summary of trxplib and plasma_state library calls used by 
trxpl2ps:

  use plasma_state_mod
  implicit NONE

  type (plasma_state) :: ss   ! state object into which to load data
  logical :: mhdeq_flag       ! .TRUE. to include the reconstructed
                              ! TRANSP MHD equilibria in returned
                              ! state objects

  integer :: ierr  ! status return code, 0=normal

  real*8 :: ttime  ! desired time point

  !---------------------------------------
  ! select a reference machine description

  call trxplib_clear_mdescr
  call trxplib_add_mdescr(<machine-description-filename>,ierr)

  !---------------------------------------
  ! initialize Plasma State object (ss) and module
  call ps_init_user_state(ss, <driver-program-name>, ierr)

  !---------------------------------------
  ! initialize trxplib library options

  call trpxlib_ps_reset
  call trxplib_mhdeq_opt(mhdeq_flag)

  !---------------------------------------
  ! select TRANSP run; error checks

  call trxplib_ps_open(<mode>,<TRANSP-path>,<output-path>,<prefix>,ierr)

    ! <mode> is a 4 character string:  "FILE" or "MDS+"
    ! <TRANSP-path> character string identifies the desired TRANSP run
    !   PPPL MDS+ example: "transpgrid.pppl.gov:TRANSP_D3D(D3D,104276B13)"
    !   PPPL FILE example: "/p/transparch/result/D3D/00/104276B13"
    !     (it is possible to access runs from non-PPPL servers as well).
    ! <output-path> directory on local file system where to write files
    !     (this can be "." for current working directory).
    ! <prefix> Plasma State suggested filename prefix -- written in
    !   "protimes.dat"

    ! ierr=0 on completion if successful
    ! <output-path>/<runid>_init.mdescr contains the TRANSP run's 
    !   machine description which may have a subset of the neutral beams
    !   in <machine-description-filename>.
    ! <output-path>/protimes.dat ... contains available times and 
    !   suggested corresponding Plasma State NetCDF filenames

  <set desired time value   ttime = ... >

  call trxplib_ps_get(ttime, ss, ierr)

    ! Plasma State object "ss" is populated with data from the open
    ! TRANSP run at the selected time.

    ! use ps_store_plasma_state to write ss to file, if desired

  call ps_free_user_state(ss, ierr)   ! cleanup, deallocate ss object

  call trxplib_ps_close               ! close connection to TRANSP run

Here are the TRANSP I/O libraries (from $NTCCHOME/lib) that need to be
linked into the driver program using this software:

(list last checked by DMC Nov. 2010):

   libtrxplib.a
   libtrread.a
   libtr_getnl.a
   librp_kernel.a
   librplot_io.a
   libxdatmgr.a
   libsplitn.a
   libtrdatbuf_lib.a
   libechmod_iolib.a
   libuflib.a
   libmds_sub.a
   libufhdf.a
   libkey_access.a

It is recommended to position these libraries prior to libplasma_state.a
in an ordered library linkage list.

An MDS+ data access library also has to be linked, at/near the end 
of the ordered library linkage list.  If a dummy version (such as 
$NTCCHOME/lib/libmds_dummy.a) is used, only the FILE access will work.

In addition the libraries needed to use Plasma State have to be linked
(but this is already the case for any driver that was already using
trxpl_server output).