BESSIM, A program for "statistical visualization" of turbulence
		spectra, (such as measured by BES on TFTR).

		by Greg Hammett, Princeton Plasma Physics Lab
			Last modified, January 30, 1993.

This is free software and comes with ABSOLUTELY NO WARRANTY.  This software
is used as a research tool, and is frequently undergoing changes.  Beware,
some of the options may no longer work properly.  Downloading and compiling
information is at the end of this document.

For information on the Beam Emission Spectroscopy data used by this
program, see "Fluctation Measurements in the Plasma Interior", R.J. Fonck,
N. Bretz, G. Cosby, R. Durst, E. Mazzucato, R. Nazikian, S. Paul, W. Tang,
M. Zarnstorff, in Plasma Physics and Controlled Fusion, Vol. 34, p 1993
(1992).

BESSIM takes the measured kx and ky spectra of turbulent fluctuations (such
as measured by BES) and generates "statistical visualizations" of the
turbulence.  These are snapshots (particular "realizations" at an instant
of time) of what the the density perturbations versus x and y might look
like.  (The (x,y) coordinates are equivalent to (r,th) coordinates as far
as this program is concerned.)  There are two main assumptions:

(1) The phases of various k-modes are assumed to be random.  (There are
also options to explore what happens if the phases are correlated in a
particular way to give intermittent, coherent structures.)

(2) The power spectrum of the fluctuations is assumed separable into the
form S(k_r,k_th) = S_r(k_r) S_th(k_th).  

It should be emphasized that although these assumptions seem innocuous
enough, they have a big impact on the results, especially the random phase
assumption.  For example, if all of the phases are zero, then one will get
a single coherent structure in the middle of the picture (you can see this
by considering the case where the spectrum is Gaussian, and realizing that
the Fourier transform of a Gaussian is also Gaussian).  By adjusting the
relative phases in a definite way, one can make this coherent structure
appear anywhere in the picture.  If this coherent structure moves around at
random, then one gets the usual spectrum where the phase of any given
k-mode is random but the relative phases of different k modes is correlated
in a specific way.  One can add a number of coherent structures randomly to
the picture, and still get the same time-averaged statistical spectrum.
One can get a range of "intermittency" in the turbulence depending on the
number of such coherent structures and the average distance between them.
In the limit that one has an infinite number of (small amplitude)
structures added at random, one should recover the random-phase picture
which has a "kurtosis" of zero (space-filling turbulence with no
intermittency, i.e., Gaussian statistics).  The kurtosis is something which
experiments should be able to measure, and hence can tell us the degree of
intermittency in the turbulence.

**************************************************************************

To look at some sample output from the program, type:

% cd ~hammett/bes
% ximage  		# and look at bes40_random.pic or bes40_40.pic

To use bessim, first edit the arrays akr and pkr to contain the S_r(k_r)
power spectrum for the fluctuations, and the arrays akth and pkth to
contain the S_th(k_th) power spectrum.  Recompile the program by typing
"make".  Then type "bessim" and enter a "," on every line to generate a
standard "statistical visualization" assuming random phases. To instead
generate a "statistical visualization" assuming coherent modes placed at
random positions in the box, type:

% bessim
Bessim, January 30, 1993 Version, by Greg Hammett, PPPL.
This is free software and comes with ABSOLUTELY NO WARRANTY.

Type a "," to get the default (in parentheses):
Radial (x) box length (cm) (40.0)?
,
Poloidal (y) box length (cm) (40.0)?
,
random or fixed phases (r or f) (r)?
f
 number of coherent modes (0=none) (40)?
40
random or fixed initial random number (r or f) (r)?
r

*************************

Once the bes.hdf file is generated, take the following steps to convert it
to a standard form which Ximage can read.

% hdfstat bes.hdf       # verifies proper hdf format of bes.hdf, though
                        # you can ignore false error message at end

% ~dcoster/bin/sun4/fptohdf bes.hdf -o bes.pic -r -i 600 600 -p tri2.pal -m 0

# This converts bes.hdf to bes.pic, expanding it (with interpolation)
# onto a 600x600 pixel array.
#
# If you instead one to view the turbulence full size, then set the
# radial and poloidal box length used by bessim to 19 cm, and
# use "-i 750 750" as an option to fptohdf. Then bes.hdf represents a 
# 19.0 cm (7.48 inch) box, so on a screen with 97 dots per inch, this comes 
# out within 10% of actual size.  Later, when run through xwdto500c, 
# it will be expanded to 3 times the number of dots in each direction, 
# and will come out actual size on the HP Deskwriter C, a 300 dpi 
# color printer.  Use smaller pixel array (like 400x400) if you
# want to animate lots of frames on your xterminal

% ximage  # to view bes.pic and play with the palette.  Alternative
          # palettes are in /usr/local/lib/ncsa/palette.

% XImage1.2.1.sn4 # For a more recent version of ximage.

% xview bes.pic  # Can't seem to get this to work!

# Need to be on Lyman for this next step to work, because the HP
# color printer is connected only to Lyman through an AppleTalk
# network:

# To print the ximage window onto a color printer, while running ximage,
# execute:
% ~hammett/bin/x_hpcolor  # prints a window to the HP color printer.

# updated HDF sources and documentation are in /scratch3/HDF.

#######################################################################
#
# To print out more copies of the popular picture, ON LYMAN type:
#
# uncompress bes40_random.500c
# source cprint
#
########################################################################

************************************************************************

Downloading and compiling information.

% tar xvf bessim.tar bessim
% compress bessim.tar
% uuencode bessim.tar.Z bessim.tar.Z > bessim.mail

bessim.mail can then be sent via email to anyone.

In the mail message is a copy of my "bessim" program I use to do
"statistical visualization" of turbulence spectra.  Put this mail message
into a file called bes.mail.  Place this in a directory where you want the
bessim directory to be.  Then type

% uudecode bes.mail
% uncompress bessim.Z
% tar xuf bessim.tar
% cd bessim
% make			# To compile the program
% more bessim.doc	# To read the documentation file
% bessim		# To run the program

BESSIM makes use of some random number generators from the NAG library
(which could be replaced by other random number generators), some HDF
routines, and the ximage tool for visualizing 2D scientific data on
X-terminals (versions also exist for the Macintosh).  Ximage is
functionally equivalent to the commercial "Spyglass" package for the
Macintosh.  HDF and XImage are available via anonymous ftp from the
National Center for Supercomputing Applications.  Alternatively, you can
write out the array den(x,y) near the end of bessim.f in any format you
want and plot it with any contour plotting package you can get your hands
on.  If you choose to try the tools from NCSA, type:

% ftp ftp.ncsa.uiuc.edu       	# or ftp 128.174.20.50
Connected to zaphod.ncsa.uiuc.edu.
220 zaphod FTP server (Version 6.23 Sun Aug 23 22:04:57 CDT 1992) ready.
Name (ftp.ncsa.uiuc.edu:hammett): anonymous
331 Guest login ok, send e-mail address as password.
Password:
ftp> get README.FIRST
ftp> quit
% more README.FIRST

Finally, the way the program is currently interfaced to HDF, you would also
need to get the fptohdf tool written by Dave Coster at PPL.  Contact him at
dcoster@theory.pppl.gov.

**********************************************************

It might actually be simpler if you just modify bessim.f near the end to
write out the array den(x,y) in any format you need.  Then you can plot it
with any contour plotting package you can get your hands on.