## Slide 1: Generic questions
New scientific insights/conceptual breakthroughs enabled by SciDAC
Changed understanding of mode ICRF conversion
  Importance of conversion to ion cyclotron wave
  Solution in 2D – gives never before seen complete picture, connects antenna to conversion region
  Textbook example of partnership of theory, experiment, computational modeling
Potential breakthroughs
  Full wave lower hybrid solutions – role of diffraction and spectral broadening
  Solutions in 3D – mode conversion, interaction with 3D plasma perturbation, MHD processes
  Arbitrary non-Maxwellian distribution in non-uniform distributions – higher dimensions
Demonstrated utilization of terascale computing
Next slide
Likelyhood of timely delivery of timely delivery of terascale computing capability modeling capabilities addressing burning plasma physics issues relevant to ITER
Certain
  We already can do fast wave calculations for relevant ITER parameters, including non-thermal effects
  We have codes capable of studying mode conversion and full wave lower hybrid on ITER (if we could get a big enough computer) – INSITE proposal being developed
  Our models are ready to be integrated with transport models and MHD and will be necessary elements for ITER scenario design and experimental interpretation

## Slide 2: Demonstrated utilization of terascale computing capability
AORSA jobs run last two weeks
And there is effective usage of terascale computers
 | Fourier space | Configuration space
Number of equations | 248,832 | 39,492
Matrix size | 990 Gbytes | 25 GBytes
Time to load matrix | 1.2 min | 7.1 min
Matrix solve (ScaLAPACK | 344 min | 3.5 min
Fourier transform | 9.5 min | 0.04 min
Total CPU time | 358 min | 13.4 min
Flops/processor | 1.1 Gflops | 0.25 Gflops
There is usage of terascale computers
AORSA is a JOULE code

## Slide 3: Generic questions
Specific steps to ensure more analysis of simulation data
Relation of solutions to simple 0D/1D wave concepts
  Local modes
  Mode conversion
  Local damping or macroscopic force
  New fundamental concepts of wave plasma interaction
Fair question we will have to think about how to do this better
Code verification – multiple code instance – AORSA/TORIC, CQL3D, Orbit/RF, direct orbit integration in Rf fields
Code validation – we have an ongoing program of comparison with experiments
What would our ideal computer look like?
We have many different mathematical operations so we need a well balanced platform
  We can’t say whether vector vs MPP scalar is better, yet – not enough experience with new vector architecture and we don’t know where the bottlenecks will be with integrated codes
There is an upper limit on memory/speed/run time required for ITER, but we can only give gross extrapolations as to what these are.
Reasonable turn around time

## Slide 4: Specific questions
What will we do to validate the quasilinear approach?
Issue 1 – decorrelation of particle orbits in RF field solutions
  Plug in numbers in Stix Chapter 14-17
  To explore other decorrelation mechanisms – direct orbit solutions and comparison
Issue 2 – linearization of Vlasov-Maxwell system that give the first order equations  nonlinear mode coupling
  Probably ok in core plasma, likely not ok in edge plasma where nonlinear effects may be present
  Part of our edge/antenna component addresses this – Time dependent PIC simulation
  Also a fair question that we will put some thought into
Does bounce average include radial motion of fast particles?
No – CQL3D is a zero orbit width code (i.e. particles stay on a flux surface). Both the collision operator and the quasilinear operator are bounce averaged with this assumption. AORSA calculates velocity space diffusion coefficients local in space and velocity space which are then bounce averaged assuming no deviation from flux surface
Plans for terascale computing applications beyond linear dense matrix solve?
Dense matrix solve in no longer the dominant computation load in AORSA
High resolution mode conversion calculations, full wave lower hybrid
Integrated models – AORSA/Fokker Planck, TORIC/TOPICA, Edge/antenna integrated models