## Slide 1: CEMM Answers to the PAC Questions
S. C. Jardin
June 3, 2005
Princeton Plasma Physics Laboratory

## Slide 2: 1. What steps are you going to take to insure that there is more analysis of the data?
Further enhance common HDF5/AVS-based M3D/ NIMROD viewer with:
  Poincare plots
  routines to analyze stochastic fields
    Beyond fractal dimension ?
Institute real-time data streaming of simulation data to local sites for visualization and analysis (Klasky, et al)
Exploring automated data management with SDM/SPA SciDAC center

## Slide 3: Characterizing Field Line Structure with Fractal Dimension
The dimensionality of a field line inside the separatrix of a tokamak provides information relevant to confinement.
  Lines tracing out irrational surfaces are two-dimensional.
  Lines tracing out rational surfaces are one-dimensional.
  Stochastic field lines are space-filling and potentially three-dimensional.
The extent to which stochastic lines fill space may give an indication of the effect of parallel heat conduction on radial transport.
A measure of non-integer dimensions in data sets is provided by the Hausdorff-Besicovitch fractal dimension
where N() is the minimum number of hypercubes of linear size  necessary to
cover all points in the set.

## Slide 4: Fractal Dimension: Good Flux Surfaces
t = 1266.17
magnetic axis

## Slide 5: Fractal Dimension: Large Islands
t = 1795.61
magnetic axis

## Slide 6: Fractal Dimension: High Stochasticity
t = 1839.86
magnetic axis

## Slide 7: Fractal Dimension: Moderate Stochasticity
t = 1944.27
magnetic axis

## Slide 8: 2. What kind of hardware and computing environment would you like?
The most important thing for “research codes” (as opposed to production codes) is that there be availability to computing platforms without long queue wait times
The NIMROD and M3D production jobs need to run for long times. They need a queuing system where they can submit long runs (24-48 hours) without waiting a long time for the job to start.
The codes perform and scale best on machines with high-performance networking and associated very low MPI latencies, like the SGI Altix
Need a seamless way to get simulation data back to local site storage for subsequent analysis and visualization. We are working on this.

## Slide 9: 3. What is your plan for addressing development of closures, including sub-gridscale models?
We have “closure experts” on our team [Callen, Ramos, Hegna, Held…] who are willing to work with the computational people in developing closures that are practical for numerical implementation.
There will be an initial closures discussion this Summer in Wisconsin to discuss this issue, and begin planning for the pre-APS workshop and the Spring 2006 workshop.
This activity will be featured topic of the CEMM meeting this fall at APS, and we expect that CEMM will become central to such activity.
We plan to organize a Closures Workshop for late winter/early spring of 2006.

## Slide 10: 4. What other Nonlinear Benchmarks will you be doing? What physics will be compared?
The CDX-U nonlinear benchmark is near completion. During the next year, we will document, assess, and publish this benchmark and determine if there is a need for a follow-up nonlinear benchmark.
The Closures Workshop and discussion may result in another non-linear benchmark calculation.

## Slide 11: 5. How will you benchmark the 2-fluid capability?
Basic wave propagation
Two-fluid effects on magnetic reconnection
Energy conservation and convergence tests
Compare ELM results with BOUT
May need to define a 2-fluid test problem. This will be discussed in Closures Workshops.

## Slide 12: 6. What are your plans to optimize your codes for the Cray X-1?
The majority of the M3D time is spent in the linear solvers, which are done with PETSc.
  Most of the solvers heavily depend on how fast the matrix-vector product can be done, particularly CG/Jacobi. The initial improvement here by ORNL helped……however,
  Still need another 10 times improvement. We are discussing with Cray how to do this. May require a PETSc interface to access an optimized Cray sparse solver
NIMROD requires either a version of SuperLU optimized to the Cray, or equivalent.
We are doing some exploratory timing studies with co-array Fortran to better understand the optimization issues with the X1. This could lead to new solvers, separate from PETSc.
The M3D-C1 code should perform well since most of the time is spent in defining the matrix elements, but it also requires SuperLU availability.
We presently do not have significant time allocated on the X1.
We are also exploring the Red Storm and IBM Blue Gene

## Slide 13: 7. What are the plans to implement AMR in the flagship codes?
We presently have 3 code lines that we will continue:
M3D
(SP-2F)
NIMROD
AMRMHD
M3D-C1
Implicit 2-fluid
Block-structured AMR, conservative finite difference
High-order finite element, spectral in 
Unstructured finite element, grid in 
Richtmeyer Meshkov
pellet injection
supersonic gas injection
reconnection
other applications ?
NIMROD
Implicit 2-fluid
Unstructured, triangles, adaptive h-refinement
Adaptation via mesh distortion without changing connectivity

## Slide 14: 8. What new scientific insights/conceptual breakthroughs have been enabled by the FES SciDAC Program
Physics of the sawtooth cycle of a small tokamak,
  including the nonlinear role of the higher toroidal harmonics.
Physics of the saturation of the Fishbone mode in a burning plasma
  , including mode chirping.
Physics of the redistribution of mass after pellet injection into a tokamak
  the difference between low and high-field side injection
Physics of the formation of closed flux surfaces in a gun-injected spheromak
  how to optimize the timings and ratios of the driving voltages
Physics of the saturation of the n=1 mode in a high- ST with co-injection
  crucial role of the 2-fluid effects
Nonlinear physics of the Edge Localized Mode (preliminary)

## Slide 15: 9. Demonstrated utilization of terascale computing capability?
Essentially all of the applications presented were performed on the IBM SP3 ( Seaborg ) at NERSC
  Several Million node-hours used. Exact amount available upon request or by checking NIM web pages.

## Slide 16: 10. Likelihood of timely delivery of reliable computational modeling capabilities addressing burning plasma physics issues relevant to ITER?
7 critical problems identified in our proposal that are important for ITER
  Sawtooth,
  Neoclassical Tearing Mode
  Resistive Wall Mode
  Energetic Particle Modes
  Edge Localized Modes
  Vertical Displacement Events
  Pellet and Supersonic Gas Jet fueling
Integration Activities will focus on ITER applications
  Integrated calculation of sawtooth stabilization/destabilization by RF (with RF SciDAC group)
  Hybrid calculation of neoclassical closures (with ORNL)
  M3D (NIMROD) are part of C.S. Cheng, et al , (R. Cohen, et al) Edge FII