## Slide 1: Physical Mechanisms Driving Gyrokinetic Turbulence
G. W. Hammett
Princeton Plasma Physics Lab (PPPL)
http://w3.pppl.gov/~hammett
Pauli Institute, Vienna
Gyrokinetic Workshop
15-19 Sept. 2008
(based on APS talk
Orlando, 11/12/2007)
Candy, Waltz (General Atomics)

## Slide 2: Physical Mechanisms Driving Gyrokinetic Turbulence
Intuitive pictures of gyrokinetic turbulence, & how to reduce it:
  analogy with inverted pendulum / Rayleigh-Taylor instability
  reducing turbulence with sheared flows, magnetic shear, plasma shaping  advanced tokamak & advanced stellarator designs

## Slide 3: Motivation & Summary

## Slide 4: Fusion performance depends sensitively on confinement
Normalized Confinement Time HH = E/Empirical
Sensitive dependence on turbulent confinement causes some uncertainties, but also gives opportunities for significant improvements, if methods of reducing turbulence extrapolate to larger reactor scales.
Caveats: best if MHD pressure limits also improve with improved confinement. Other limits also: power load on divertor & wall, …
0
5
10
15
20
Q = Fusion Power / Heating Power

## Slide 5
Intuitive pictures of gyrokinetic turbulence, & how to reduce it
  analogy w/ inverted pendulum / Rayleigh-Taylor instability
  reduce turbulence with sheared flows, magnetic shear, …
effective
gravity
Inverted-density fluid
Rayleigh-Taylor Instability

## Slide 6
  (many of these insights developed with gyrofluid simulations in 1990’s, but gyrokinetics provides higher accuracy.)
Intuitive pictures of gyrokinetic turbulence, & how to reduce it

## Slide 7
Stable Pendulum
L
M
F=Mg
=(g/L)1/2
Unstable Inverted Pendulum
= (-g/|L|)1/2 = i(g/|L|)1/2 = i
g
L
(rigid rod)
Density-stratified Fluid
stable=(g/L)1/2
=exp(-y/L)
Max growth rate=(g/L)1/2
=exp(y/L)
Inverted-density fluid
Rayleigh-Taylor Instability
Instability

## Slide 8: “Bad Curvature” instability in plasmas  Inverted Pendulum / Rayleigh-Taylor Instability
Top view of toroidal plasma:
plasma = heavy fluid
B = “light fluid”
geff = centrifugal force
R
Growth rate:
Similar instability mechanism
in MHD & drift/microinstabilities
1/L = p/p in MHD,
 combination of n & T
in microinstabilities.

## Slide 9
The Secret for Stabilizing Bad-Curvature Instabilities
Twist in B carries plasma from bad curvature region
to good curvature region:
Unstable
Stable
Similar to how twirling a honey dipper can prevent honey from dripping.

## Slide 10: Spherical Torus has improved confinement and pressure limits (but less room in center for coils)

## Slide 11
These physical mechanisms can be seen
in gyrokinetic simulations and movies
Unstable bad-curvature
side, eddies point out, direction of effective gravity
particles quickly move along field lines, so density perturbations are very extended along fields lines, which twist to connect unstable to stable side
Stable
side, smaller eddies

## Slide 12
Movie http://fusion.gat.com/THEORY/images/3/35/D3d.n16.2x_0.6_fly.mpg from http://fusion.gat.com/theory/Gyromovies shows contour plots of density fluctuations in a cut-away view of a GYRO simulation (Candy & Waltz, GA). This movie illustrates the physical mechanisms described in the last few slides. It also illustrates the important effect of sheared flows in breaking up and limiting the turbulent eddies. Long-wavelength equilibrium sheared flows in this case are driven primarily by external toroidal beam injection. (The movie is made in the frame of reference rotating with the plasma in the middle of the simulation. Barber pole effect makes the dominantly-toroidal rotation appear poloidal..) Short-wavelength, turbulent-driven flows also play important role in nonlinear saturation.
Sheared
flows

## Slide 15
Rosenbluth-Longmire picture

## Slide 16
Rosenbluth-Longmire picture
Can repeat this analysis on the good
curvature side & find it is stable.
(Leave as exercise.)

## Slide 17: Simple picture of reducing turbulence by negative magnetic shear
Particles that produce an eddy tend to follow field lines.
Reversed magnetic shear twists eddy in a short distance to point in the ``good curvature direction''.
Locally reversed magnetic shear naturally produced by squeezing magnetic fields at high plasma pressure: ``Second stability'' Advanced Tokamak or Spherical Torus.
Shaping the plasma (elongation and triangularity) can also change local shear
Fig. from Antonsen, Drake, Guzdar et al. Phys. Plasmas 96
Kessel, Manickam, Rewoldt, Tang Phys. Rev. Lett. 94
(in std tokamaks)
“Normal” in stellarators
Advanced Tokamaks

## Slide 18: Selected Gyrokinetic References
This talk available at w3.pppl.gov/~hammett/talks
3 GYRO movies shown (d3d.n16.2x_06_fly, n32o6d0.8, & ETG-ki) from http://fusion.gat.com/theory/Gyromovies
Web sites for 4 main gyrokinetic codes discussed here (incl. refs., documentation):
  GYRO (Waltz & Candy, GA): fusion.gat.com/theory/Gyro
  GS2 (Dorland & Kotschenreuther, U. Maryland/Texas): gs2.sourceforge.net
  GENE (Jenko, Garching): www.ipp.mpg.de/~fsj
  GEM (Parker & Chen, U. Colorado): cips.colorado.edu/simulation/gem.htm
“Anomalous Transport Scaling in the DIII-D Tokamak Matched by Supercomputer Simulation”, J. Candy & R. E. Waltz, Phys. Rev. Lett. 2003
“Burning plasma projections using drift-wave transport models and scalings for the H-mode pedestal”, Kinsey et al., Nucl. Fusion 2003
“Electron Temperature Gradient Turbulence”, W. Dorland, F. Jenko, M. Kotschenreuther, B.N. Rogers, Phys. Rev. Lett. 2000
“Generation & Stability of Zonal Flows in Ion-Temperature-Gradient Mode Turbulence”, Rogers, Dorland, Kotschenreuther, Phys. Rev. Lett. 2000
"Comparisons and Physics Basis of Tokamak Transport Models and Turbulence Simulations", Dimits et al., Phys. Plasmas 2000.
“Simulations of turbulent transport with kinetic electrons and electromagnetic effects”, Y. Chen, S.E. Parker, B.I. Cohen, A.M. Dimits et al., Nucl. Fus. 43, 1121 (2003)

## Slide 19: Selected Gyrokinetic References (cont.)
Brizard & Hahm, Reviews of Modern Physics 2007
“A Short Introduction to General Gyrokinetic Theory”, H. Qin, in Fields Institute Communications 46, Topics in Kinetic Theory, American Mathematical Society, 171 (2005). see also http://www.pppl.gov/~hongqin/QinPapers.php
“Geometric Gyrokinetic Theory for Edge Plasmas”, H. Qin, R. H. Cohen, W. M. Nevins, and X. Q. Xu, Physics of Plasmas 14, 056110 (2007)
“Theory and Computation in Full-F Gyrokinetics” B. D. Scott, Princeton PPL Theory seminar, June 2005, and other useful presentations at http://www.ipp.mpg.de/~bds/
E. A. Frieman and L. Chen, Phys. Fluids 25, 502 1982
T. M. Antonsen and B. Lane, Phys. Fluids 23, 1205 1980
P. J. Catto, W. M. Tang, and D. E. Baldwin, Plasma Phys. 23, 639 (1981)
D. H. E. Dubin, J. A. Krommes, C. Oberman, & W. W. Lee, Phys. Fluids 26, 3524 (1983)
T. S. Hahm, Phys. Fluids 31, 2670 (1988)
A. Brizard, J. Plasma Phys. 41, 541 (1989)
A. M. Dimits, L. L. Lodestro, and D. H. E. Dubin, Phys. Fluids B 4, 274 (1992)
W.W. Lee, Phys. Fluids 26, 556 (1983)
"Astrophysical Gyrokinetics: Basic Equations and Linear Theory," Gregory G. Howes, Steven C. Cowley, William Dorland, Gregory W. Hammett, Eliot Quataert, Alexander A. Schekochihin, Ap.J 651, 590 (2006), astro-ph/0511812

## Slide 20: Acknowledgements:
J. Candy & R. E. Waltz (GA) (GYRO results & movies)
W. Dorland (Univ. Maryland), M. Kotschenreuther (U. Texas)
F. Jenko (Garching)
S. Cowley (UCLA)
W. Nevins, B.I. Cohen, A.M. Dimits, R. Cohen (LLNL)
S.E. Parker and Y. Chen (U. Colorado)
B. D. Scott (Garching)
Hong Qin (PPPL)
T.S. Hahm, A. Brizard, W.W. Lee, W. Tang, J. Krommes, T. Stoltzfus-Dueck
Chris Holland, Anne White, Jon Kinsey, Gary Staebler
D. Ernst, D. Mikkelsen, R. Budny
Center for Multiscale Plasma Dynamics
DOE Scientific Discovery Through Advanced Computing (SciDAC)
  Center for the Study of Plasma Microturbulence
  Edge Simulation Laboratory
  Earlier DOE SciDAC & Computational Grand Challenge projects, including Plasma Microturbulence Project & Numerical Tokamak Project
DOE National Energy Research Supercomputing Center (NERSC)
Many others…