## Slide 1: TITLE
Stuart R.Hudson, D.A.Monticello, A.H.Reiman, D.J.Strickler, S.P.Hirshman, L-P. Ku, E.Lazarus, A.Brooks, M.C.Zarnstorff, A.H.Boozer, G-Y. Fu and G.H.Neilson.
Suppression of Magnetic Islands In Stellarator Equilibrium Calculations.
Application to NCSX.
19th IAEA Fusion Energy Conference
Lyon, France 14-19 October 2002

## Slide 2: Motivation and Outline.
Stellarators will in general have islands and, unless avoided or suppressed, islands and associated regions of chaos lead to poor plasma confinement.
Islands in free-boundary NCSX equilibria were eliminated (coil-healing) as a final step in the coil design, after the coil-plasma optimization.
Details of the coil healing procedure are described.
4) Results for NCSX are presented showing a stable stellarator equilibrium, with build-able coils, with “good-flux-surfaces”.

## Slide 3: Coils are modified to remove islands.
original equilibrium
with islands and chaos
`healed’ equilibrium
with good surfaces
coil adjustment
to remove resonant fields
(not to scale)
2cm

## Slide 4: Coil healing is required because …
The plasma and coils are designed using optimization routines that shape plasma boundary to achieve desired physics, while satisfying engineering constraints on coil geometry. (see Strickler IAEA-CN-94/FT/P2-06)
All fast equilibrium codes (in particular VMEC) presuppose perfect nested magnetic surfaces  existence & size of magnetic islands cannot be addressed.
After the plasma and coil optimization, the coil geometry is modified to suppress the spectrum of B.n relevant to island formation  this procedure is called coil-healing.
Coil-healing must not degrade the optimized plasma properties (ideal stability, quasi-axisymmetry, aspect ratio, . . . ).
Coil-healing must not violate engineering constraints.

## Slide 5: The equilibrium calculation and coil healing proceed simultaneously via an iterative approach.
1) Bn = BPn + BC(n)
2) p = J(n+1)  Bn
3) J(n+1) =   BP
4) BP(n+1) =BPn+(1- )BP
5) B = BP(n+1) + BC(n)
6) –Ri= RCij  nj
7) j (n+1) = jn + jn
At each iteration, the coil geometry is adjusted
to cancel the resonant fields
n iteration index ; BP plasma field ; BC coil field ;  coil geometry harmonics ;
=0.99 blending parameter ; RCij coupling matrix.
A single PIES/healing iteration is shown
coil geometry adjusted
resonant fields function of 
nearly integrable field
total field = plasma + coil field
calculate plasma current
calculate plasma field
blending for numerical stability
Based on the PIES code

## Slide 6: Rational surfaces are located.
Quadratic-flux minimizing surfaces may be thought of as rational rotational transform flux surfaces of a nearby field with good flux surfaces. Dewar, Hudson & Price.Physics Letters A, 194:49, 1994 Hudson & Dewar, Physics of Plasmas 6(5):1532,1999.
Resonant normal fields at the rational surfaces form islands, and island overlap causes chaos.
Island suppression achieved by suppression of resonant fields.
perturbation
shear field
+
island chain

## Slide 7: The field normal to the rational surface is calculated.
Cross section (black line)
passes through island
Poincare plot on =0 plane
(red dots)
=0 plane
For given BP, the resonant normal
field is a function of coil geometry
n
B = BP + BC()
e
e
illustration of
quadratic-flux-minimizing surface

## Slide 8: Resonant fields are cancelled by coil-adjustment; engineering constraints and plasma stability is preserved.
The coil-coil separation and coil minimum radius of curvature are functions of coil-geometry .
Ideal stability (kink, ballooning) are functions of free-boundary equilibrium, which in turn is a function of coil-geometry .
The desired solution is R = 0.
coil/plasma resonant fields
engineering constraints
ideal stability
initial values

## Slide 9: Standard numerical methods find solution R=0.
First order expansion for small changes in 
A multi-dimensional Newton method solves for the coil correction to cancel the resonant fields at the rational surface
The coil geometry is adjusted     .
At each PIES iteration, the coils are adjusted to remove resonant fields.
As the iterations proceed, the coil field and plasma field converge to an equilibrium with selected islands suppressed.

## Slide 10: The healed configuration has good-flux-surfaces.
3/6 island suppressed
high order islands
not considered.
VMEC initialization
boundary
Poincare plot on
up-down symmetric
=2/6
3/5 island suppressed
reference state
 = 4.1%
I = 178kA
(0) = 0.40
(1) = 0.65

## Slide 11: The magnitude of the coil change is acceptable.
plot shows coils on toroidal winding surface
coil change  2cm
coil change exceeds
construction tolerances
does not impact machine design (diagnostic, NBI access still ok)
* the resonant harmonics have been adjusted
original
healed

## Slide 12: The healed coils support good vacuum states.
The healed coils maintain good vacuum states
first wall

## Slide 13: Healed coils show improvement as configuration varies
 as  and profiles vary, the island content will vary;
the island content of the healed coil equilibria is acceptable
(improved respect to the original coils),
for a sequence of equilibria modeling a discharge evolution;
discharge scenario
t = 303ms
 = 4.58%
I = 132kA
(0) = 0.307
(1) = 0.655
`healed’ coils;
smaller (3,5) island
original coils;
large (3,5) island

## Slide 14: Trim Coils provide additional island control
without trim coils:
(n,m)=(3,6) island
with trim coils:
island suppressed
discharge scenario
t = 100ms
 = 3.38%
I = 81.6kA
(0) = 0.427
(1) = 0.511
the same procedure determines the trim coil currents which suppress islands

## Slide 15: Summary
The plasma and coils converge simultaneously to a free-boundary equilibrium with selected islands suppressed, while preserving engineering constraints and plasma stability.
Adjusting the coil geometry at every PIES iteration enables effective control of non-linearity of the plasma response to changes in the external field.
Coils support a variety of equilibria with good flux surface quality, and trim coils provide control of islands.