## Slide 1: Influence of pressure-gradient and average-shear on ballooning stability semi-analytic expression for ballooning growth rate
S.R.Hudson1, C.C.Hegna2, N.Nakajima3, R.Torasso4, A.Ware5, J.G.Wohlbier2
1) Princeton Plasma Physics Laboratory, P.O. Box 451,Princeton NJ 08543, USA.
2) Department of Engineering Physics, University of Wisconsin-Madison, WI 53706, USA.
3) National Institute for Fusion Science, Nagoya 464-01, Japan.
4) Courant Institute of Mathematical Sciences, New York University, NY 10012, USA.
5) Department of Physics and Astronomy, University of Montana, Missoula, MT, 59812, USA.
TH/P2-24 : 20th IAEA Fusion Energy Conference, 1-6 November 2004, Vilamoura, Portugal

## Slide 2: Motivation
Recent work on 2nd stability in stellarators has shown that
  some stellarators do [WARE et al., PRL 2002],
  some stellarators do not [HEGNA & HUDSON, PRL 2001],
  possess 2nd stable regions.
What property of the configuration determines 2nd stability ?
Outline
The method of profile variations [GREENE & CHANCE, NF 1983] is applied to stellarator configurations [HEGNA & NAKAJIMA, PoP 1996].
The profile variations (and the self-consistent coordinate response) produce variations in the ballooning coefficients.
Eigenvalue perturbation theory is used to obtain an analytic expression for the ballooning growth rate,  , as a function of the pressure-gradient and average-shear: =  (' ,p ') (for constant geometry).
The analytic expression determines if pressure-gradient is stabilizing or destabilizing, and suggests if a 2nd stable region will exist.

## Slide 3: Three approaches will be compared
Equilibrium reconstruction
  multiple equilibrium calculations
  (vary p'() & '(); VMEC)
  multiple ballooning calculations
Profile-variations
[GREENE&CHANCE,1983]
  single equilibrium calculation
  (construct semi-analytic equilibria)
  multiple ballooning calculations
Analytic expression
(extension of profile-variations)
  single equilibrium calculation
  single ballooning calculation
pressure gradient
average shear
to be described

## Slide 4: The pressure-gradient and average-shear profiles are varied (method of profile variations)
We begin with a full solution to an MHD equilibrium (VMEC)
An analytic variation in p &  is imposed
 is formally small parameter
b is surface of interest
variation in the gradients is zero-order in 
two free parameters (, p )

## Slide 5: The self-consistent coordinate response is determined
later will keep (')2, (' p'), (p')2 , .
the coordinates are similarly adjusted to preserve p=JB :
To zero order in , the local shear is changed
This equation is :
  exact at the surface of interest;
  valid for arbitrarily large (, p );
  the coefficients are determined by the original equilibrium:

## Slide 6: The coefficients of the ballooning equation are changed
may be resolved numerically;
but further analytic progress possible

## Slide 7: Eigenvalue perturbation theory gives analytic expression for change in ballooning growth rate
operator inversion
inner product
operator inversion

## Slide 8: The theory determines . . . • if increased p' is stabilizing or destabilizing, • if a 2nd stable region will exist.
valid if 3/p'3 p' << 2/p'2 ; in general, need (p')3,(p')4, . , .
unstable
2nd stable
1st stable

## Slide 9: Marginal stability boundary : quasi-poloidal configuration
quasi-poloidal configuration [WARE et al. PRL, 2002] has 2nd stable region
solid curve is stability boundary determined by exactly re-solving ballooning equation on grid 200x200
dotted curve from analytic expression
  including 2nd order terms
  single eigenfunction calculation
analytic expression accurately reproduces exact stability boundary

## Slide 10: Stability boundary is verified by global equilibrium reconstruction
a sequence of increasing pressure equilibria is constructed with VMEC
  fixed boundary, fixed current profile
For each s=0.3 surface, the ballooning stability is re-calculated
  indicated with  or +, stable or unstable
The marginal stability diagram is constructed
  using original equilibrium O
    solid : exact solution to perturbed eqn.
    dotted : from 2nd order analytic expression
The stability diagram gives good prediction of global stability boundary
unstable
2nd stable
1st stable

## Slide 11: In general, need higher order terms . . • LHD-like configuration • NCSX-like configuration
solid : exact (numerical) solution to perturbed ballooning equation
dotted : from analytic expression (2nd order)
dashed : from analytic expression (4th order)

## Slide 12: Summary
An analytic expression describing the dependence of the ballooning growth rate on pressure-gradient and shear variations is derived.
The expression agrees well with the exact numerical solution to the perturbed ballooning equation, and agrees with stability boundaries computed with global equilibrium reconstructions.
The expression determines :
  if pressure-gradient is stabilizing or destabilizing
  suggests if a 2nd stable region will exist.
Theory may be of use in stellarator optimization routines and enable deeper insight into mechanism of 2nd stability.