## Slide 1: Stepped pressure profile equilibria via partial Taylor relaxation
R. L. Dewar1, M. J. Hole1, S. R. Hudson2
[1] Research School of Physical Sciences and Engineering, Australian National University, ACT 0200, Australia
[2] Princeton Plasma Physics Laboratory, New Jersey 08543, U.S.A.
Supported by Australian Research Council Grant DP0452728

## Slide 2: Contents
MHD equilibria in 3D
Project Aims
A stepped pressure profile model
  Cylindrical plasma equilibria and stability
  Ongoing work : generalization to arbitrary geometry
Summary

## Slide 3
1. 3D MHD equilibria
Ideal MHD model
3D MHD equilibria are solutions of ideal MHD in systems with no (spatial) ignorable co-ordinates
Tokamaks, due to coil ripple or instabilities:
E.g. Stellarators:
Astrophysical plasmas:

## Slide 4: Winding Numbers for Toroidal Magnetic Fields
In tokamaks, conventionally use winding number q =  / 2 
q = irrational: B ergodically passes through all points in magnetic surface.
q = rational (m/n) : B lines close on each other.
(ie. toroidal B rotations per poloidal B rotation)
In stellarators, use rotational transform :


In tokamaks, and ideally in stellarators, B lies in magneticsurfaces, which field lines cover by winding around in a helical fashion

## Slide 5: In general 3D MHD equilibria, p  0 and smoothness of profiles are incompatible:

But B. is a very singular operator: either  blows up at each rational magnetic surface (which would be dense, if they existed), or •J = 0 densely. Suff. to take
Set
,  arb. const. along field lines
“In order to have a static (3D) equilibrium, p’() must be zero in the neighborhood of every rational rotational transform, and flux surfaces must be relinquished”
Cf. Grad, Toroidal Containment of plasma, Phys. Plas. 10 (1967)
Solution:
. Then
So, to ensure a mathematically well-defined J, we set p = 0 over finite regions  B = B — force-free field

## Slide 6: Beltrami & piecewise Beltrami
Force-free fields for which  = const over a volume are called Beltrami fields
Strong field-line chaos in a region implies a Beltrami field in region since  = const on a field line, and a single field line fills a chaotic regions ergodically
Even if there are islands in the region, Beltrami assumption is natural, as it is the simplest equilibrium solution
If there are surfaces separating chaotic regions,  and p can jump across such surfaces

## Slide 7
1. Hamiltonian mechanics  B solutions:
Perturbs an integrable Hamiltonian p within a torus T0 (flux surface) by a periodic functional perturbation p1:
3. Bruno and Laurence (c. 1996, Comm. Pure Appl. Maths, XLIX, 717-764, )
Derived existence theorems for sharp boundary solutions for tori for small departure from axisymmetry.
KAM theory : if flux surface are sufficiently far from resonance (q sufficiently irrational), some flux surfaces survive for  < c
KAM surfaces
 step the pressure only across KAM surfaces.
2. Kolmogorov Arnold Moser (KAM) Theory (c. 1962)
H = p, t = 
p = , q = 
s



## Slide 8: Approximation of smooth profiles : E.g. Cylindrical Equilibria
p but can be made arbitrarily close to a smooth function by letting number of steps go to , step height to 0. Not differentiable, but no significant generality has been lost.

## Slide 9: 2. Project Aims
design a convergent algorithm for constructing 3D equilibria,
  solve a 50-year old fundamental mathematical problem
  quantify relationship between magnitude of departure from axisymmetry and existence of 3D equilibria
  provide a better computational tool for rapid design and analysis
explore relationship between ideal MHD stability of multiple interface model and internal transport barrier formation
in MAST …M. J. Hole et al., PPCF, 2005
Courtesy JAERI

## Slide 10
In 1974, Taylor argued that turbulent plasmas with small resistivity and viscosity relax to a Beltrami field, B = B
i.e. solutions to W = 0 of functional :
Internal energy:
Taylor solved for minimum U subject to fixed H
Total Helicity :
I
P
V
3. Taylor relaxation
(where <> denotes jump across interface I)
We invoke field-line chaos rather than turbulence, and generalize to partially relaxed plasmas.

## Slide 11: Extension to multiple interfaces : Frustrated Taylor Relaxation
Generalization of single interface model :
- Spies et al Relaxed Plasma-Vacuum Systems, Phys. Plas. 8(8). 2001
- Spies. Relaxed Plasma-Vacuum Systems with pressure, Phys. Plas. 8(8). 2003
potential energy functional:
helicity functional:
mass functional:
loop integrals conserved
New system comprises:
N plasma regions Pi in relaxed states.
Regions separated by ideal MHD barrier Ii.
Enclosed by a vacuum V,
Encased in a perfectly conducting wall W
…
I1
In-1
In
V
Pn
P1
W

## Slide 12: Partial relaxation using ideal invariants—earlier work
Like Bhattacharjee & Dewar, Energy Principle with Global Invariants, Phys. Fluids 25, 887 (1982) in that we constrain relaxation with an extended class of weighted helicities that are all invariant under ideal MHD perturbations
Differ from B&D in using step-function weights

## Slide 13: 1st variation “relaxed” equilibria
Energy Functional W:
Setting 1W = 0 yields:
n = unit normal to interfaces I, wall W
Poloidal flux pol, toroidal flux t constant during relaxation:

## Slide 14: 2nd variation  stable equilibria
+ expressions for perturbed fluxes, pol , t in each region.
. Yields
Minimize 2W, wrt fixed constraint. Two possible choices are
NB :
b = B
n = ·n
 = interface displacement vector
Find solutions of
with

## Slide 15: 3.1 Eg: Cylindrical Equilibria
I1
I2
IN
W
P1
P2
PN
IN-1
V
…
Solutions to
barriers at radial locations ri ,
BV, BzV, ki, di,  
Jm, Ym are Bessel functions
 Total # unknowns = 4N+1
Variables | # unknowns
k1…kN | N
d2…dN | N-1
1… N | N
r1… rN-1, rW | N
BV, BzV | 2

## Slide 16: Equilibria with positive shear exist
Eg. five-layer equilibrium solution
Contours of poloidal flux p
q profile continuous in plasma regions,
core must have some reverse shear
Not optimized to model tokamak-like equilibria

## Slide 17: Spectral Analysis  B solutions
Fourier decompose perturbed field b and interfaces 
are complex Fourier amplitudes
m  Z,   2 Z /Lz, Lz periodicity axial length
In Pi, V, system of equations reduce to :
and L
with
Solns in Pi, V, of form
2N + 2 unknown constants : c11, c12,…cN1, cN2, cV1,cV2
- BC’s at wall and core eliminate two unknowns
- Apply 1st interface condition 2N times (inside + outside)

## Slide 18: Interface conds  eigenvalue equation
Second interface condition
First interface condition at each interface Ii
ci1, ci2 = f(Xi-1, Xi)

For N interfaces reduces to tridiagonal eigenvalue equation

## Slide 19: Stability benchmarked to 1-layer results
Use QR algorithm for Hessenberg matrices to solve for all eigenvalues [Numerical Recipes, Ch. 11]
Benchmark 1-layer equilibrium scans to Kaiser and Uecker, reproducing stability boundaries
EG.  = 0 scan over Lagrange multiplier () and jump in B angle at plasma/vacuum interface () for different conducting wall radii rl . Regions interior to each layer contour are stable.
Kaiser and Uecker, X1 fixed (N=0)
Hole, Dewar, Hudson

## Slide 20: Configuration space contracts with increasing beta
Finite  scan over Lagrange multiplier () and jump in B angle at plasma/vacuum interface () for wall radius rl =1.1.
Regions interior to each layer contour are stable.

## Slide 21: ITB Configurations
+ constrain q1i = q1o
& rITB from solution of

## Slide 22: Configuration Scan

## Slide 23: 3D Beltrami field—first cut
Weakly perturb plasma boundary:
Poincaré plot of B
using method of lines.
Some chaos visible.
Solve

## Slide 24: 4. Summary 1/2
Flux surfaces support increases in pressure.
High performance (ie. high pressure) fusion plasmas require good flux surfaces.
Ab initiio: in 3D ideal MHD,
  p = 0 in regions of rational q,
  flux surfaces must be relinquished for rational qs.
For highly irrational q, some flux surfaces survive.
Project aims :
  design a convergent algorithm for constructing 3D ideal MHD equilibria,
  explore relationship between ideal MHD stability of multiple interface model and internal transport barrier formation

## Slide 25: Summary 2/2
(6) Analytic stepped pressure equilibria have been constructed and studied in cylindrical geometry
- different normalization give ballooning/ global stability
- code written to compute global stability… analysis in progress
(7) numerical algorithms to solve in arbitrary 3D geometry to be designed and implemented.