## Slide 1: A stepped pressure profile model for internal transport barriers
M. J. Hole1, S. R. Hudson2, R. L. Dewar1, M. McGann1 and R. Miills1
[1] Research School of Physical Sciences and Engineering, Australian National University, ACT 0200, Australia
[2] Princeton Plasma Physics Laboratory, New Jersey 08543, U.S.A.
Supported by Australian Research Council Grant DP0452728
Acknowledgements : Useful discussion / input from Brian Taylor (FRS), Robert MacKay (FRS), Chris Gimblett, Allan Boozer

## Slide 2: Contents
Motivation
  - MHD equilibria in 3D
  - Proposed solution for 3D MHD equilibria: stepped Beltrami equilibria
  - Model applications to internal transport barriers
  - Project aims
Variational principle for a stepped pressure profile model
  - Equilibria
  - Stability
Generalised Taylor cylindrical plasmas
- Equivalence to tearing mode treatment
- Ideal/Taylor cylindrical plasmas
4. A model for internal transport barriers
5. Summary

## Slide 3: 1. Toroidal plasma equilibrium in 3D
Good model for toroidal fusion plasma steady state is force balance for total pressure p combined with Ampère’s law relating magnetic field B and current density J:
and Tokamaks, (also 3D due to coil ripple or instabilities):
EG Stellarators—intrinsically 3D, i.e. no continuous symmetry:
Magnetic fields are in general fully 3D

## Slide 4: 3D Equilibrium Problems
Problems:
A. In 3D plasmas, magnetic islands form on rational flux surfaces, destroying flux surface
  Field is chaotic within magnetic islands, and ergodically fills island volume
  Fortunately… not all flux surfaces are destroyed
B. 3D MHD equilibria have current singularities if p  0
Current 3D MHD solvers built on premise that volume is foliated with toroidal magnetic flux surfaces (eg. VMEC1 ), &/or adapts magnetic grid to try to compensate (PIES2)
Can not rigorously solve ideal MHD – error usually manifest as a lack of convergence3,4.
1 S. P. Hirshman and Whitson, Phys. Fluids 26, 3553 1983.
2 A. H. Reiman and H. S. Greenside, J. Comput. Phys. 75, 423 1988.
3 H. J. Gardner and D. B. Blackwell, Nucl. Fusion 32, 2009 1992.
4 S.R. Hudson, M.J. Hole and R.L. Dewar, Phys. Plasmas 14, 052505 (2007)

## Slide 5: A. 3D MHD field is, in general, chaotic
Field lines can be described as a 1½ DOF Hamiltonian
H =    , t = 
p = , q = 
If axisymmetric, Hamiltonian is autonomous
(ie.      )
If non axis-symmetric , Hamiltononian is non-autonomous     and the field is in general non-integrable.
  Magnetic islands form at rational (), in which field is stochastic or chaotic, ergodically filling the island volume.
  Bp=0  confinement lost in these islands.
= irrational: B ergodically passes through all points in magnetic surface.
 = rational (m/n) : B lines close on each other.
Eg. B Poincaré sections in H-1, courtesy S. Kumar

## Slide 6: Some sufficiently irrational magnetic flux surfaces survive 3D perturbation
Perturbs an integrable Hamiltonian p within a torus (flux surface) by a periodic functional perturbation p1:
KAM theory : if flux surface are sufficiently far from resonance (q sufficiently irrational), some flux surfaces survive for  < c
Kolmogorov Arnold Moser (KAM) Theory (c. 1962)
Bruno and Laurence (c. 1996, Comm. Pure Appl. Maths, XLIX, 717-764, )
Derived existence theorems for sharp boundary solutions for tori for small departure from axisymmetry.
 stepped pressure profile solutions can exist.
Maximising number of good flux surfaces is the topic of advanced stellarator design S. R. Hudson et al Phys. Rev. Lett. 89, 275003, 2002

## Slide 7: Standard map captures breakdown of surfaces
Properties of 3D field captured by standard map:
For N’th toroidal orbit:
3D perturbation parameter
k=0

s


s
s
k=0.9
k=1.1
Increasing destruction of flux surfaces
For k>0.98 no surfaces (extending over all ) exist

## Slide 8: B. Current singularities exist in 3D equilibria
General Case :

For rational , (B. ) in 3D is a singular operator  J||  
To remove singular currents we require . J =0 p=0
With solution
&  constant on field lines
To see singularity of (B. ) operator, Fourier expand (B. ) in magnetic coordinates (, m, )
Radial coordinate
(const  surface)
Toroidal angle
( = const locus on constant  torus)
Poloidal angle
( = const locus on constant  torus)
 = average toroidal flux but field lines do not necessarily lie within this torus.

## Slide 9: Singularity of (B.) operator
Fourier expand (B. ) in magnetic coordinates (, m, )
() = rotational transform (=1/q)
= poloidal / toroidal transit of field
If () =n/m, then (B. )=0, and so
We require p=0 for rational (),
J|| singularity removed
Eg. ITER field lines
NB: For a tokamak, only 0m is nonzero, & problem vanishes

## Slide 10: Recap: 3D Equilibrium Problems
Problems:
A. In 3D plasmas, magnetic islands form on rational flux surfaces, destroying flux surface
  Field is chaotic within magnetic islands, and ergodically fills island volume
  Fortunately… not all flux surfaces are destroyed
B. 3D MHD equilibria have current singularities if p  0
“In order to have a static (3D) equilibrium, p’() must be zero in the neighborhood of every rational rotational transform, and flux surfaces must be relinquished”
cf. Grad, Toroidal Containment of plasma, Phys. Plas. 10 (1967)
Problem B not new…

## Slide 11: Proposed solution: Stepped-pressure Beltrami equilibria
Pros
  Beltrami eqn. is a linear elliptic PDE, solvable by variety of methods even if B has chaotic regions
  Has already been partially investigated mathematically [e.g. Bruno & Laurence, Comm. Pure Appl. Math. XLIX, 717 (1996)]
Cons (?)
  Pressure profile not differentiable (but may approximate a smooth profile arbitrarily closely, limited only by existence of invariant tori)
To ensure a mathematically well-defined J, we set p = 0 over finite regions  B = B,  = const (Beltrami field) separated by assumed invariant tori.
Different  in each region

## Slide 12: Force balance on invariant tori
Pressure discontinuous: [[p]]  0 (where [[]] is jump across an invariant torus), but total pressure, magnetic plus kinetic, is continuous: [[p+B2/2]] = 0
-function p
 sheet current J
discontinuity in B (both magnitude & direction)
winding number  not necessarily same on either side of invariant torus (not standard KAM problem)
If constructed as a variational problem, may have other applications…
NB: Beltrami or force free field initially inspired by Astrophysical research, Chandrasekhar, Woltjer et al.

## Slide 13: Internal Transport Barriers
Plasmas with radially localised regions of improved confinement with steep pressure gradients1. Typically,
  non-monotonic q profile
  q rationality plays a role (eg. appearance of q=2 can promote ITB formation in JET)
Most theoretical models rely on suppression of micro-instability induced transport by sheared EB flows.. however do not offer an energetic reason for ITB formation
1J. W. Connor et al, Nuc. Fus. 44, R1-R49, 2004.

## Slide 14
Also in MAST …M. J. Hole et al., PPCF, 2005
ETB
ITB
#7085 at 290ms

## Slide 15: Variational Model for ITB’s
Idea: perhaps a variational formulation (min. energy states) of a relaxed plasma-vacuum system may offer insight into why the ITB forms
Trial pressure profile, field in each region Beltrami

## Slide 16: Builds on recent variational models of ETB’s
A relaxed plasma-vacuum model has been recently applied to Edge Transport Barriers to describe the ELM cycle:
  Cylindrical geometry assumed
  Toroidal peeling modes initiate Taylor relaxation
  Taylor relaxation flattens torodial current profile, further destabilising peeling mode, but…
  Stabilising edge skin current also formed by relaxation
  Balance between destabilising and stabilising terms determines width of the ELM.
1 C. G. Gimblett et al PRL, 035006, 96, 2006

## Slide 17: Project Aims
design a convergent algorithm for constructing 3D equilibria,
  solve a 50-year old fundamental mathematical problem
  quantify relationship between magnitude of departure from axisymmetry and existence of 3D equilibria
  provide a better computational tool for rapid design and analysis
(2) explore relationship between ideal MHD stability of multiple interface model and internal transport barrier formation
NB: Group is investigating different methods to construct 3D equilibria:
Variational Approach, method of lines/shooting method1 , Hamilton–Jacobi equation for surface magnetic potentials, Hamiltonian trial function. This talk will focus on an energy variational approach.
1 S.R. Hudson, M.J. Hole and R.L. Dewar, Phys. Plasmas 14, 052505 (2007)

## Slide 18
In 1974, Taylor argued that turbulent plasmas with small resistivity, and viscosity relax to a Beltrami field
i.e. solutions to W=0 of functional :
Internal energy:
Taylor solved for minimum U subject to fixed H
Total Helicity :
I
P
V
Zero pressure gradient regions are force-free magnetic fields:
2. A Stepped Pressure Profile Model

## Slide 19: Generalised Taylor Relaxation 1/2
subject to finite number of ideal-MHD constraints (unlike ideal MHD where flux and entropy are “frozen in” to each fluid element — infinite no. of constraints).
Require constraints to be a subset of the ideal-MHD constraints, so generated states are ideal equilibria:
Ideal MHD: infinity of constraints
Relaxed MHD: finite no. of constraints
Spaces of allowed variations:
Idea: Extremize total energy
Kruskal–Kulsrud equilibria — include Taylor states
Generalized Taylor equilibria
cf. A. Bhattacharjee and R.L. Dewar, Phys. Fluids 25, 887 (1982) Energy principle with global invariants

## Slide 20
potential energy functional:
helicity functional:
mass functional:
New system comprises:
N plasma regions Pi in relaxed states.
Regions separated by ideal MHD barrier Ii.
Enclosed by a vacuum V,
Encased in a perfectly conducting wall W
…
I1
In-1
In
V
Pn
P1
W
Generalised Taylor Relaxation 2/2
toroidal and poloidal fluxes: i and i
Assume each invariant tori Ii act as ideal MHD barriers to relaxation, so that Taylor constraints are localized to subregions.

## Slide 21: 1st variation “relaxed” equilibria
Energy Functional W:
Setting W=0 yields:
n = unit normal to interfaces I, wall W
Poloidal flux pol, toroidal flux t constant during relaxation:

## Slide 22: 2nd variation stable equilibria
+ expressions for perturbed fluxes, pol , t in each region.
. Yields
Minimize 2W, wrt fixed constraint. Two possible choices are
NB :
b = B
n = ·B
 = interface displacement vector
Find solutions of
with

## Slide 23: 3.Generalized Taylor Relaxed Cylindrical Plasmas
…
R
rw
rN=1
r1
rN-1
Each region Pi has Lagrange multiplier i, pressure pi
At interface I, safety factor on inner and outer sides is i, o
I1
IN-1
IN

## Slide 24: B solutions produce eigenvalue problem
Cylindrical solutions are Bessel functions:
with unknowns: coeffs. ki, di; interface radii ri; vacuum field.
4N+1 unknowns can be cast as constraint set:
This is an eigenvalue1 problem for i.
with
1 S. R. Hudson, M. J. Hole, R. L. Dewar Phys. Of Plas., 14, 052205, 2007
or

## Slide 25: Eigenvalues for Beltrami multiplier
Eg. Constrain 1=2, r1=0.5, r2=1  solutions of 2 are multi-valued in 2
Fundamental: continuous  in r1<r< r2
1st harmonic: (r) one pole in r1<r< r2
2nd harmonic: (r) two poles in r1<r< r2
Eigenvalues versus 2
Rotational transform radial profile

## Slide 26: Equilibria with positive shear exist
Eg. 5 layer equilibrium solution
Contours of poloidal flux p
q profile smooth in plasma regions,
core must have some reverse shear
Not optimized to model tokamak-like equilibria
M. J. Hole, S. R. Hudson and R. L. Dewar, J. Plasma Phys., 72, 1167, 2006

## Slide 27: Approximating continuous pressure gradients
Eg. 5 layer equilibrium solution
Contours of poloidal flux p
arbitrary number of steps can be used to model “real” data
3D proviso : barriers located at irrational q
p is piecewise smooth.

## Slide 28: Spectral Analysis  eigenvalue problem
Fourier decompose perturbed field b and interfaces i
are complex Fourier amplitudes
m  Z,   2 Z /Lz, Lz periodicity axial length
In Pi, V, ODE’s solved: eg in Pi
2(N + 1) unknown constants ci1, c,i2
- BC’s at wall and core eliminate 2 unknowns
- Apply 1st interface condition 2N times (inside + outside)
2nd interface condition reduces to form
choice of N2 has shifted Alfvén continuum to 
# solutions for lambda = N

## Slide 29: Cylindrical Example: Stability
For N interfaces reduces to eigenvalue equation
For N=1, reproduces calculations of Kaiser and Uecker, Q. Jl of Appl. Math. 57(1), 2004
m=1
m=2
Marginal stability boundaries (=0) for m=1 and m=2

= jump in pitch across interface


M. J. Hole, S. R. Hudson, R. L. Dewar, Nuc. Fusion, 47, 2007
Stable region interior to locii
Stable region exterior to locii

## Slide 30: Benchmarking multi-interface stability
Consider two similar plasma regions, with 1= 2
Dispersion curves match for N=1 and N=2 in limit of vanishing interface separation r = r2 – r1
r1
r2
rw
Unstable configuration studied
2-02
02=0


m=1

## Slide 31: N=2: Stability differs if q is C0, even if r0
Aim: Investigate stability of plasma with q continuous across second plasma region (adjust 2 to match q at r1, r2)
Motivation: Eliminate singular current on interface (infinite current density) by removing jump in q
Result: For r 0, N=2 unstable, while N=1 stable. Physically, r 0 requires 2   new current sheet in P2.
2<0
2
2
P1
P2
I1
I2

## Slide 32: Resolving the edge pressure (R. Mills et al)
Aim: What is the effect of resolving edge pressure gradient?
Path: In P2 make plasma ideal with nonzero ramp in pressure
  need to solve explicitly for (r), as b = (B)
  produces Euler-Lagrange equation for  (r)
  resonances must be handled explicitly1
1Newcomb, Annals of Phys. 10, 232-267, 1960
Taylor-Taylor treatment allows resistive modes in P2 as r0.
Taylor-ideal, and Taylor do not.
reson in P2 | N=2 |  | N=1
 | Taylor-Taylor | Taylor-Ideal | Taylor
 | 2<0 | 2>0 | 2>0
 | 2>0 | 2>0 | 
  Ideal: helicity per field line conserved
  Taylor: helicity in each volume conserved
Result:

## Slide 33: Modes of generalized Taylor relaxation
What unstable modes allowed by these generalized Taylor states?
- modes of ideal MHD, current driven except at interfaces (where pressure driven modes can exist)
- tearing modes
Ideal MHD: infinity of constraints
Relaxed MHD: finite no. of constraints
Spaces of allowed variations:
Kruskal–Kulsrud equilibria — include Taylor states
Generalized Taylor equilibria
Recent work by Tassi et al investigate tearing mode stability of force-free equilibria:
Motivation: MHD activity often observed in RFP’s with well defined value of m/n, equal to central resonance (quasi-singular helicity states). Taylor’s theory suggests entire plasma should relax via modes with multiple-helicity (m/n)
Tassi , Hastie and Porcelli Phys. Plas., 14, 092109, 2007

## Slide 34: Tearing modes of force-free equilibria
Tassi et al Phys. Plas., 14, 092109, 2007
We generalize model for multiple interfaces, inclusion of vacuum and to enable pressure jumps.
Tassi et al
Assume two plasma regions, no vacuum, and no pressure
Conclude presence of downward step in q (lamda) destablises innermost mode, and suggest possible cyclic mechanism for QSH relaxation

## Slide 35: Tearing mode vs. Taylor stability
generalize model for multiple interfaces, inclusion of vacuum and to enable pressure jumps.
Does tearing mode and variational principle stability agree? YES
q
r
0
0.1
1
1.1
-0.05
’→
Variational eigenvalues
tearing modes
m=1
m=1
’→
external kink
Internal kink

## Slide 36: A model for Internal Transport Barriers
reverse shear profile cylindrically periodic plasma assumed
Choose qmin, q0 and qedge chosen,
Stability computed for these configurations
Appeal to toroidal mode number discretisation to tune system to eliminate unstable modes.
In limit that m→, n →. Is anything stable left?
Scan over qmin, q0
Investigate pressure profile dependence
Equilibrium constraints:

## Slide 37: In progress: Exploration of ITB’s
2<q100<4 stable
marginal stability
internal mode
external mode
m=2

## Slide 38: Other approaches to constructing 3D equilibria
Development of iterative algorithms to solve Beltrami fields in 3D geometry (S.Hudson et al )
  - noting  is an eigenvalue, simultaneously solve for  and B (method of lines / shooting method)
  - adjust interface to reduce force imbalance
Motivation: Solve Beltrami fields in 3D configurations
Surface current equilibria formulation. (M. McGann)
Generalize treatment of Kaiser and Salat Phys. Plasmas 1(2), 1994, who
  parameterise an interface surface S.
  select B=0 interior to S, and B =  exterior to S,
  substitute B into force balance  PDE for 
  search for S which allow an analytic solution for .
Motivation: Provides method to construct toroidal flux surfaces, and establish robustness to pressure difference

## Slide 39: 4. Summary 1/2
Explanation of problem:
- flux surfaces wanted for good confinement
- in general, they are rare in 3D geometry
(2) Project aims :
- design a convergent algorithm for constructing 3D equilibria
- are ITB’s in a constrained minimum energy state?
(3) Variational model developed – frustrated Taylor relaxation
(4) Analytic solutions presented for a cylinder
  - Equilibria with positive shear exist
  - Stability: benchmarked for N=1, stable configurations for N>1 exist without jumps in q if appeal to discretisation
  - Need to be careful with resonances if trying to construct jumps in q from multi-interface with continuous q
  - stability of variational problem in multi-interfaces can be reduced to stability of tearing + ideal modes

## Slide 40: 4. Summary 2/2
(5) Exploration of ITB-like configurations underway. Seeks to scan over qmin, q0 and qedge, utilise toroidal/poloidal discretisation and determine whether any stable modes left in the limit of m→, n →
(6) Various algorithms to solve in arbitrary 3D geometry based on stepped pressure profile now being developed.