## Slide 1: Theory and numerics of partially-relaxed, topologically-constrained, MHD equilibria with chaotic magnetic fields Stuart Hudson Princeton Plasma Physics Laboratory R.L. Dewar, M.J. Hole & M. McGann The Australian National University 20th International Toki Conference, 7-10 December 2010, Toki, Japan
Motivation & Outline
→ The simplest model of approximating global, macroscopic force balance in toroidal plasma confinement with arbitrary geometry is magnetohydrodynamics (MHD)
→ As toroidal magnetic fields are analogous to 1-1/2 Hamiltonians, and are generally chaotic, we need an MHD equilibrium code that allows for chaotic fields.
→ Existing ideal MHD equilibrium codes with chaotic fields fail to accommodate the fractal structure of Hamiltonian chaos. This leads to an ill-posed numerical algorithm for computing numerically-intractable, pathological equilibria.
→ A new partially-relaxed, topologically-constrained MHD equilibrium model is described and implemented numerically. Results demonstrating convergence tests, benchmarks, and non-trivial solutions are presented.
Notes: <number>

## Slide 2: Ideal-force-balance with chaotic field is pathological
Diophantine condition
Kolmogorov, Arnold and Moser
→ transport of pressure along field is “infinitely” fast
→ no scale length in ideal MHD
→ pressure adapts exactly to structure of phase space
→ cannot be inverted to obtain parallel current
Notes: <number>

## Slide 3: Taylor relaxation: a weakly resistive plasma will relax, subject to single constraint of conserved helicity
Ideal MHD equilibria and Taylor-relaxed equilibria are at opposite extremes . . . .
Ideal-MHD → imposition of infinity of ideal MHD constraints
non-trivial pressure profiles, but structure of field is over-constrained
Taylor relaxation → imposition of single constraint of conserved global helicity
structure of field is not-constrained, but pressure profile is trivial, i.e. under-constrained
We need something in between . . .
. . . perhaps an equilibrium model with finitely many ideal constraints, and partial Taylor relaxation?
linear force-free field ≡ Beltrami field
But, . . .Taylor relaxed fields have no pressure gradients
Notes: <number>

## Slide 4: Introducing the multi-volume, partially-relaxed model of MHD equilibria with topological constraints
V4
V3
V2
V1
ideal interfaces coincide with KAM surfaces
→ field remains tangential to interfaces,
→ a finite number of ideal constraints,
imposed topologically!
Notes: <number>

## Slide 5: Topological constraints : pressure gradients coincide with flux surfaces
→ structure of B and structure of the pressure are intimately connected;
→ cannot apriori specify pressure without apriori constraining structure of the field;
Notes: <number>

## Slide 6
→ how large the “sufficiently small” departure from axisymmetry can be needs to be explored numerically . . . .
Notes: <number>

## Slide 7: Extrema of energy functional obtained numerically; introducing the Stepped Pressure Equilibrium Code, SPEC
piecewise cubic or quintic basis polynomials
minimal spectral width [Hirshman, VMEC]
solved using sparse linear solver
adjusted so interface transform is strongly irrational
future work . . .
approximate derivative matrix ~ 2nd variation of energy functional
implement pre-conditioner
Notes: <number>

## Slide 8: Numerical error in Beltrami field scales as expected
h = radial grid size = 1 / N
n = order of polynomial
Poincaré plot, =0
(m,n)=(3,1) island
+ (m,n)=(2,1) island
= chaos
quintic, n=5
cubic, n=3
Example of chaotic Beltrami field
Poincaré plot, =π
Notes: <number>

## Slide 9: stepped-pressure equilibria accurately approximate smooth-pressure axisymmetric equilibria
cylindrical Z
cylindrical R
cylindrical R
cylindrical Z
lower half = SPEC interfaces
upper half = SPEC & VMEC
increasing pressure
increasing pressure resolution ≡ number of interfaces
N ≡ finite-element resolution
magnetic axis vs. radial resolution
using quintic-radial finite-element basis
(for high pressure equilibrium)
(dotted line indicates VMEC result)
toroidal flux 
Pressure, p
toroidal flux 
stepped-profile approximation to smooth profile
transform
Notes: <number>

## Slide 10: Equilibria with (i) perturbed boundary→chaotic fields, and (ii) pressure are computed .
high-pressure equilibrium
β  4%
zero-pressure equilibrium
β = 0%
Convergence of (2,1) & (3,1) island widths with Fourier resolution for β  4% case
(2,1) island
(3,1) island
← island widths estimated by fitting quasi-rational surface through island chain
poloidal angle
radial coordinate
Notes: <number>

## Slide 11: Summary
→ A partially-relaxed, topologically-constrained energy principle has been presented for MHD equilibria with chaotic fields and non-trivial (i.e. non-constant) pressure
→ The model has been implemented numerically
* using a high-order (piecewise quintic) radial discretization
* an optimal (i.e. spectrally condensed) Fourier representation
* workload distrubuted across multiple cpus,
* extrema located using Newton’s method with quadratic-convergence
→ Intuitively, the equilibrium model is an extension of Taylor relaxation to multiple volumes
→ The model has a sound theoretical foundation
* solutions guaranteed to exist (under certain conditions)
→ The numerical method is computationally tractable
* does not invert singular operators
* does not struggle to resolve fractal structure of chaos
→ Convergence studies have been performed
* expected error scaling with radial resolution confirmed
* detailed benchmark with axisymmetric equilibria (with smooth profiles)
* that the island widths converge with Fourier resolution has been confirmed
Notes: <number>

## Slide 12
Notes: <number>

## Slide 13: Toroidal magnetic confinement depends on flux surfaces
magnetic field lines wrap around toroidal “flux” surfaces
rational field-line  = 0.3333… 
irrational field-line  = 0.3819… 
periodic poloidal angle 
periodic toroidal angle 
family of periodic orbits ≡ rational flux surface
magnetic field is called integrable
periodic poloidal angle 
Notes: <number>

## Slide 14: Ideal MHD equilibria are extrema of energy functional
→ two surface functions, e.g. the pressure, p(s) , and rotational-transform ≡ inverse-safety-factor, (s) ,
and → a boundary surface ( . . for fixed boundary equilibria . . . ) ,
constitute “boundary-conditions” that must be provided to uniquely define an equilibrium solution
. . . . . . The computational task is to compute the magnetic field that is consistent with the given boundary conditions . . .
V ≡ global plasma volume
→ magnetic differential equations are singular at rational surfaces (periodic orbits)
→ pressure-driven “Pfirsch-Schlüter currents” have 1/ x type singularity
→  - function singular currents shield out islands
→ideal variations don’t allow field topology to change “frozen-flux”
Notes: <number>

## Slide 15: Topological constraints : pressure gradients coincide with flux surfaces
→ structure of B and structure of the pressure are intimately connected;
→ cannot apriori specify pressure without apriori constraining structure of the field;
→ where there are significant pressure gradients,
there can be no islands or chaotic regions with width > ∆wc
Notes: <number>

## Slide 16: A sequence of equilibria with increasing pressure and perturbed boundary are computed
movie of sequence of equilibria with increasing pressure
Notes: <number>